## Slide 1
EEL4712 Digital Design
(Carry Lookahead Adder)

## Slide 2: VHDL Design Styles
Components and
interconnects
structural
VHDL Design
Styles
dataflow
Concurrent
statements
behavioral (sequential)
Registers
State machines
Instruction decoders
Sequential statements
Subset most suitable for synthesis
Testbenches

## Slide 3: Register Transfer Level (RTL) Design Description
Combinational
Logic
Combinational
Logic
Registers
…
Today’s Topic

## Slide 4
MLU Example

## Slide 5: MLU Block Diagram
B
A
NEG_A
NEG_B
IN0
IN1
IN2
IN3
OUTPUT
SEL1
SEL0
MUX_4_1
L0
L1
NEG_Y
Y
Y1
A1
B1
MUX_0
MUX_1
MUX_2
MUX_3
0
1
0
1
0
1

## Slide 6: MLU: Entity Declaration
LIBRARY ieee;
USE ieee.std_logic_1164.all;
ENTITY mlu IS
PORT(
NEG_A : IN STD_LOGIC;
NEG_B : IN STD_LOGIC;
NEG_Y : IN STD_LOGIC;
A : IN STD_LOGIC;
B : IN STD_LOGIC;
L1 : IN STD_LOGIC;
L0 : IN STD_LOGIC;
Y : OUT STD_LOGIC
);
END mlu;

## Slide 7: MLU: Architecture Declarative Section
ARCHITECTURE mlu_dataflow OF mlu IS
SIGNAL A1 : STD_LOGIC;
SIGNAL B1 : STD_LOGIC;
SIGNAL Y1 : STD_LOGIC;
SIGNAL MUX_0 : STD_LOGIC;
SIGNAL MUX_1 : STD_LOGIC;
SIGNAL MUX_2 : STD_LOGIC;
SIGNAL MUX_3 : STD_LOGIC;
SIGNAL L: STD_LOGIC_VECTOR(1 DOWNTO 0);

## Slide 8: MLU - Architecture Body
BEGIN
A1<= NOT A WHEN (NEG_A='1') ELSE
A;
B1<= NOT B WHEN (NEG_B='1') ELSE
B;
Y <= NOT Y1 WHEN (NEG_Y='1') ELSE
Y1;
MUX_0 <= A1 AND B1;
MUX_1 <= A1 OR B1;
MUX_2 <= A1 XOR B1;
MUX_3 <= A1 XNOR B1;
L <= L1 & L0;
with (L) select
Y1 <= MUX_0 WHEN "00",
MUX_1 WHEN "01",
MUX_2 WHEN "10",
MUX_3 WHEN OTHERS;
END mlu_dataflow;

## Slide 9
Buffers

## Slide 10
(b) Equivalent circuit
(c) Truth table
x
f
e
(a) A tri-state buffer
0
0
1
1
0
1
0
1
Z
Z
0
1
f
e
x
x
f
e
= 0
e
= 1
x
f
Tri-state Buffer

## Slide 11
Four types of Tri-state Buffers

## Slide 12: Tri-state Buffer – example (1)
LIBRARY ieee;
USE ieee.std_logic_1164.all;
ENTITY tri_state IS
PORT ( ena: IN STD_LOGIC;
input: IN STD_LOGIC;
output: OUT STD_LOGIC
);
END tri_state;

## Slide 13: Tri-state Buffer – example (2)
ARCHITECTURE dataflow OF tri_state IS
BEGIN
output <= input WHEN (ena = ‘1’) ELSE ‘Z’;
END dataflow;

## Slide 14
Wire and Buses

## Slide 15: Merging wires and buses
SIGNAL a: STD_LOGIC_VECTOR(3 DOWNTO 0);
SIGNAL b: STD_LOGIC_VECTOR(4 DOWNTO 0);
SIGNAL c: STD_LOGIC;
SIGNAL d: STD_LOGIC_VECTOR(9 DOWNTO 0);
d <= a & b & c;
4
5
10
a
b
c
d

## Slide 16: Splitting buses
SIGNAL a: STD_LOGIC_VECTOR(3 DOWNTO 0);
SIGNAL b: STD_LOGIC_VECTOR(4 DOWNTO 0);
SIGNAL c: STD_LOGIC;
SIGNAL d: STD_LOGIC_VECTOR(9 DOWNTO 0);
a <= d(9 downto 6);
b <= d(5 downto 1);
c <= d(0);
4
5
10
a
b
c
d

## Slide 17
Carry Lookahead Adders

## Slide 18: Introduction
There are many ways to implement a digital function, but each approach may have different tradeoffs
As a digital designer, you need to consider these tradeoffs when meeting design requirements
As an example, we’ll look into different adder architectures and their tradeoffs
  Read Section 5.4 for more details

## Slide 19: Ripple Carry Adder
Full Adder (FA)
Ripple Carry Adder
  A ripple carry (RC) adder is a series of full adders connected by the carry bit

## Slide 20: Advantage: Area Impact
The ripple carry adder’s area grows linearly with bit width
Each additional bit adds another full adder and its associated gates
Chart: Width
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
RC | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
+5 gates
+5 gates
+5 gates
+5 gates

## Slide 21: Disadvantage: Delay Impact
The ripple carry adder’s delay also grows linearly with bit width
Each full adder must wait for the previous full adder to produce outputs
  Lower performance with bit width!
Chart: Width
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
RC | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27 | 30
C1@3Δ
C2@5Δ
C3@7Δ
C4@9Δ

## Slide 22: Delay Problem
Delay is dependent on the carry bit “rippling” through each adder
Can we quickly determine the previous carry’s value and reduce delay?

## Slide 23: Simplifying Carry Equation
Let’s first simplify how we look at the carry equation
  Carry equation:
  Simplified:
How is carry determined in a given adder stage?
  Adder generates a carry based on gi
    When gi = 1, ci+1 = (1) + pici = 1
  Adder propagates previous carry based on pi
    When pi = 1, ci+1 = gi + (1)ci = gi + ci

## Slide 24: Generate/Propagate Example
1
0001
+1011
0
0011
0001
+1011
1100
11
0001
+1011
00
Example: 0001 + 1011
  Generate signals ()
    FA0 generates a carry ()
  Propagate signals ()
    FA1 asserts its carry () by propagating FA0’s carry ()
    FA3 de-asserts its carry () by propagating FA2’s carry ()

## Slide 25: Carry Substitution
Let’s use substitution to see how the carry bit, ci+1, is impacted by an earlier adder stage
Carry equation for adder i+1 and i:
  , or
With substitution
ci

## Slide 26: Carry Pattern
Carry Equation:
Substitutions:
c1
c2

## Slide 27: Removing Dependencies
The carry signal (ci+1) is now determined by an earlier adder stage’s carry (ci-1, ci-2).
is dependent on the following:
  The current stage generating a carry (
  The current stage propagating a generated carry from a previous stage ( or ()
  The current and previous stages propagating a carry from an earlier stage () or ()
We can perform substitution for each carry bit
Case 1
Case 2
Case 3
Case 1
Case 2
Case 3

## Slide 28: New Carry Dependence
Through substitution, every carry signal can be a function of solely c0, x, and y
  Can determine carry when inputs are ready
  Avoids waiting for the carry to ripple (ci-1)
  Three logic level delay
    Produce and terms from and
    Produce carry minterms (e.g. , , and )
    Produce final carry terms (ci) from minterms

## Slide 29: Carry Lookahead Adder (CLA)
carry minterms
propagate/generate terms
carry term
[1]
Steps
  Produce and terms from and
  Produce carry minterms (e.g. , , and )
  Produce final carry terms (ci) from minterms
All carry terms calculated concurrently and independent of previous carry calculation

## Slide 30: Constant Delay
The propagation delay is now constant, even as the adder width increases!
  Each of the CLA adder stages calculate its outputs concurrently
  By contrast, RC ripples carry through each stage and has a variable delay based on width
Chart: Width
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
RC | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27 | 30
CLA | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3

## Slide 31: Area Cost
Area now grows quadratically with width
  Propagate/generate logic grows with each stage
  Not practical for larger adders
Chart: Width
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
RC | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
CLA | 5 | 11 | 19 | 29 | 41 | 55 | 71 | 89 | 109 | 131

## Slide 32: Other Tradeoffs?
We know of two adders with different advantages as width increases
  The ripple carry’s area grows linearly, but suffers from linear growth in delay
  The carry lookahead’s delay is constant, but suffers from quadratic growth in area
Use hybrid architecture to limit both area and delay growth?

## Slide 33: Hybrid Approach
Make a ripple carry architecture out of multi-bit CLAs adders, or CLA blocks
  E.g. 4-bit CLA adders connected in a ripple carry fashion

## Slide 34: Area Impact
The hybrid adder’s area grows linearly
  Additional bits add another CLA adder and its associated gates
  Slower area growth than pure CLA, but larger area than pure RC
Chart: Width
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
RC | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50
CLA | 5 | 11 | 19 | 29 | 41 | 55 | 71 | 89 | 109 | 131
Hybrid | 5 | 11 | 19 | 29 | 34 | 40 | 48 | 58 | 63 | 69

## Slide 35: Delay Impact
The hybrid adder’s delay grows linearly
  Each CLA adder must wait for the previous CLA adder to produce outputs
    But no longer on a bit-by-bit basis!
  Lower delay growth than pure RC
Chart: Delay
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
RC | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27 | 30
CLA | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
Hybrid | 3 | 3 | 3 | 3 | 6 | 6 | 6 | 6 | 9 | 9

## Slide 36: Alternative Hierarchical Approach
In the hybrid approach, we use the RC architecture on multi-bit CLA adders
Alternatively, we can also use the CLA architecture with multi-bit CLA adders
  Use CLA architecture to gain constant delay as width increases
  Must determine propagate and generate logic on a CLA block-basis

## Slide 37: Another Look at Carry Equations
Let’s simplify how we look at the carry eq for CLA blocks
Carry equation for 4-bit CLA block:
Simplified:
How is each block’s carry determined?
  CLA block generates a carry based on Gi
    Last stage in CLA block generates a carry (g3)
    Other stages generate a carry that is propagated by later stages
  CLA block propagates previous carry based on Pi
    Each stage in CLA block propagates the input carry (p3p2p1p0)

## Slide 38: Hierarchical Carry Substitution
Let’s use substitution to see how the carry bit is impacted by earlier CLA blocks
Carry equation for CLA block 1 and 2:
With substitution
Similar to regular CLA

## Slide 39: Hierarchical Substitutions
With four 4-bit CLA blocks,
    ()
Similar to regular CLA substitutions

## Slide 40: Removing Dependencies
The carry signal (c8) is now determined by an earlier CLA block’s carry (c0).
is dependent on the following:
  The current stage generating a carry ( or
  The current stage propagating a generated carry from a CLA block ( or ()
  The current and previous stages propagating a carry from an earlier CLA block () or ()
We can perform substitution for each CLA carry bit
Case 1
Case 2
Case 3
Case 1
Case 2
Case 3

## Slide 41: Hierarchical CLA
Steps
  Produce and terms from and
  Produce and terms from and
  Produce carry minterms (e.g. , , and )
  Produce final carry terms (ci) from minterms
Figure 2. A hierarchical carry-lookahead adder [1]
carry terms (steps 3 & 4)
propagate/generate terms (steps 1 & 2)

## Slide 42: Hierarchical CLA
Compared to pure CLA
  Smaller quadratic area growth
    Block propagate/generate logic extracts common propagate/generate terms
    Avoids duplicating gates for common propagate/generate terms in each carry equation
  Larger constant delay due to block propagate/generate logic.
Figure 2. A hierarchical carry-lookahead adder [1]

## Slide 43: Practical Limitations
At larger bit-widths, the carry equations requires gates with many inputs
  Fan-in limits the number of inputs on a gate
  A network of smaller gates can be used to avoid fan-in at the cost of additional delay
E.g.
Signals may have large fan-out as well
  May need to duplicate gates to limit fan-out which increases area cost
Ideally
Practically

## Slide 44: Multi-level Hierarchical Approaches
Similar to the past two architectures, we can add additional hierarchical levels for different area/delay tradeoffs
  May help with fan-in/fan-out as width increases
  Ideal number of levels dependent on width

## Slide 45: Conclusions
Two adder architectures with different area/delay tradeoffs
  Ripple carry adder
  Carry lookahead adder
Two hierarchical architectures with different area/delay tradeoffs
  Hybrid architecture
  Hierarchical CLA
Questions?

## Slide 46: References
Stephen Brown and Zvonko Vranesic. 2004. Fundamentals of Digital Logic with VHDL Design with CD-ROM (2 ed.). McGraw-Hill, Inc., New York, NY, USA.
http://www.gstitt.ece.ufl.edu/courses/spring19/eel4712/index.html
https://ece.gmu.edu/coursewebpages/ECE/ECE545/F10/viewgraphs/ECE545_lecture5_dataflow.pdf

## Slide 47: Questions?