## Slide 1
EEL4712 Digital Design
(Modeling of Circuits with Regular Structure)

## Slide 2
Generate Scheme for Equations

## Slide 3
Example 1: PARITY: Block Diagram
Example 1: Block Diagram

## Slide 4
PARITY: Entity Declaration
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY parity IS
PORT(
  parity_in : IN STD_LOGIC_VECTOR(7 DOWNTO 0);
  parity_out : OUT STD_LOGIC
);
END parity;

## Slide 5
ARCHITECTURE parity_dataflow OF parity IS
SIGNAL xor_out: std_logic_vector (6 downto 1);
BEGIN
  xor_out(1) <= parity_in(0) XOR parity_in(1);
  xor_out(2) <= xor_out(1) XOR parity_in(2);
  xor_out(3) <= xor_out(2) XOR parity_in(3);
  xor_out(4) <= xor_out(3) XOR parity_in(4);
  xor_out(5) <= xor_out(4) XOR parity_in(5);
  xor_out(6) <= xor_out(5) XOR parity_in(6);
  parity_out <= xor_out(6) XOR parity_in(7);
END parity_dataflow;
PARITY: Architecture

## Slide 6
ARCHITECTURE parity_dataflow OF parity IS
SIGNAL xor_out: STD_LOGIC_VECTOR (6 DOWNTO 1);
BEGIN
  xor_out(1) <= parity_in(0) XOR parity_in(1);
  G1: FOR i IN 2 TO 6 GENERATE
  xor_out(i) <= xor_out(i-1) XOR parity_in(i);
  END GENERATE;
  parity_out <= xor_out(6) XOR parity_in(7);
END parity_dataflow;
PARITY: Architecture (2a)

## Slide 7
ARCHITECTURE parity_dataflow OF parity IS
SIGNAL xor_out: STD_LOGIC_VECTOR (6 DOWNTO 1);
BEGIN
  G2: FOR i IN 1 TO 7 GENERATE
    left_xor: IF i=1 GENERATE
      xor_out(i) <= parity_in(i-1) XOR parity_in(i);
    END GENERATE;
    middle_xor: IF (i >1) AND (i<7) GENERATE
      xor_out(i) <= xor_out(i-1) XOR parity_in(i);
    END GENERATE;
    right_xor: IF i=7 GENERATE
      parity_out <= xor_out(i-1) XOR parity_in(i);
    END GENERATE;
  END GENERATE;
END parity_dataflow;
PARITY: Architecture (2b)

## Slide 8: PARITY: Block Diagram (2)

## Slide 9: PARITY: Architecture
ARCHITECTURE parity_dataflow OF parity IS
SIGNAL xor_out: STD_LOGIC_VECTOR (7 downto 0);
BEGIN
  xor_out(0) <= parity_in(0);
  xor_out(1) <= xor_out(0) XOR parity_in(1);
  xor_out(2) <= xor_out(1) XOR parity_in(2);
  xor_out(3) <= xor_out(2) XOR parity_in(3);
  xor_out(4) <= xor_out(3) XOR parity_in(4);
  xor_out(5) <= xor_out(4) XOR parity_in(5);
  xor_out(6) <= xor_out(5) XOR parity_in(6);
  xor_out(7) <= xor_out(6) XOR parity_in(7);
  parity_out <= xor_out(7);
END parity_dataflow;;

## Slide 10: PARITY: Architecture (2)
ARCHITECTURE parity_dataflow OF parity IS
SIGNAL xor_out: STD_LOGIC_VECTOR (7 DOWNTO 0);
BEGIN
xor_out(0) <= parity_in(0);
G2: FOR i IN 1 TO 7 GENERATE
xor_out(i) <= xor_out(i-1) XOR parity_in(i);
END GENERATE G2;
parity_out <= xor_out(7);
END parity_dataflow;

## Slide 11: For Generate Statement
For Generate
Label:
For identifier In range GENERATE
{Concurrent Statements}
END GENERATE;
A label is compulsory with a generate statement.

## Slide 12: Conditional Generate Statement
If Generate
Label:
IF Boolean_expression GENERATE
{Concurrent Statements}
END GENERATE;
A label is compulsory with a generate statement.

## Slide 13
Generate Scheme for Components

## Slide 14
Example 1

## Slide 15
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY mux4to1 IS
  PORT ( w0, w1, w2, w3 : IN STD_LOGIC ;
  s : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
  f : OUT STD_LOGIC ) ;
END mux4to1 ;
ARCHITECTURE Dataflow OF mux4to1 IS
BEGIN
  WITH s SELECT
  f <= w0 WHEN "00",
  w1 WHEN "01",
  w2 WHEN "10",
  w3 WHEN OTHERS ;
END Dataflow ;
A 4-to-1 Multiplexer

## Slide 16
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY Example1 IS
  PORT ( w : IN STD_LOGIC_VECTOR(0 TO 15) ;
  s : IN STD_LOGIC_VECTOR(3 DOWNTO 0) ;
  f : OUT STD_LOGIC ) ;
END Example1 ;
Straightforward code for Example 1

## Slide 17
ARCHITECTURE Structure OF Example1 IS
  COMPONENT mux4to1
    PORT ( w0, w1, w2, w3 : IN STD_LOGIC ;
    s : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
    f : OUT STD_LOGIC ) ;
  END COMPONENT ;
SIGNAL m : STD_LOGIC_VECTOR(0 TO 3) ;
BEGIN
  Mux1: mux4to1 PORT MAP ( w(0), w(1), w(2), w(3), s(1 DOWNTO 0), m(0) ) ;
  Mux2: mux4to1 PORT MAP ( w(4), w(5), w(6), w(7), s(1 DOWNTO 0), m(1) ) ;
  Mux3: mux4to1 PORT MAP ( w(8), w(9), w(10), w(11), s(1 DOWNTO 0), m(2) ) ;
  Mux4: mux4to1 PORT MAP ( w(12), w(13), w(14), w(15), s(1 DOWNTO 0), m(3) ) ;
  Mux5: mux4to1 PORT MAP ( m(0), m(1), m(2), m(3), s(3 DOWNTO 2), f ) ;
END Structure ;
Straightforward code for Example 1

## Slide 18
ARCHITECTURE Structure OF Example1 IS
  COMPONENT mux4to1
    PORT ( w0, w1, w2, w3 : IN STD_LOGIC ;
    s : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
    f : OUT STD_LOGIC ) ;
END COMPONENT ;
SIGNAL m : STD_LOGIC_VECTOR(0 TO 3) ;
BEGIN
  G1: FOR i IN 0 TO 3 GENERATE
  Muxes: mux4to1 PORT MAP (
  ………, …………., …………, …………, …………, ………… ) ;
  END GENERATE ;
Mux5: mux4to1 PORT MAP ( m(0), m(1), m(2), m(3), s(3 DOWNTO 2), f ) ;
END Structure ;
Modified code for Example 1

## Slide 19
ARCHITECTURE Structure OF Example1 IS
  COMPONENT mux4to1
    PORT ( w0, w1, w2, w3 : IN STD_LOGIC ;
    s : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
    f : OUT STD_LOGIC ) ;
END COMPONENT ;
SIGNAL m : STD_LOGIC_VECTOR(0 TO 3) ;
BEGIN
  G1: FOR i IN 0 TO 3 GENERATE
    Muxes: mux4to1 PORT MAP (
    w(4*i), w(4*i+1), w(4*i+2), w(4*i+3), s(1 DOWNTO 0), m(i) ) ;
  END GENERATE ;
Mux5: mux4to1 PORT MAP ( m(0), m(1), m(2), m(3), s(3 DOWNTO 2), f ) ;
END Structure ;
Modified code for Example 1

## Slide 20
Example 2

## Slide 21
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY dec2to4 IS
  PORT ( w : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
  En : IN STD_LOGIC ;
  y : OUT STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
END dec2to4 ;
ARCHITECTURE Dataflow OF dec2to4 IS
SIGNAL Enw : STD_LOGIC_VECTOR(2 DOWNTO 0) ;
BEGIN
  Enw <= En & w ;
  WITH Enw SELECT
  y <= "0001" WHEN "100",
  "0010" WHEN "101",
  "0100" WHEN "110",
  􀀁1000" WHEN "111",
  "0000" WHEN OTHERS ;
END Dataflow ;
A 2-to-4 binary decoder

## Slide 22
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY dec4to16 IS
  PORT (w : IN STD_LOGIC_VECTOR(3 DOWNTO 0) ;
  En : IN STD_LOGIC ;
  y : OUT STD_LOGIC_VECTOR(15 DOWNTO 0) ) ;
END dec4to16 ;
VHDL code for Example 2 (1)

## Slide 23
VHDL code for Example 2 (1)
ARCHITECTURE Structure OF dec4to16 IS
  COMPONENT dec2to4
    PORT ( w : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
    En : IN STD_LOGIC ;
    y : OUT STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
  END COMPONENT ;
SIGNAL m : STD_LOGIC_VECTOR(3 DOWNTO 0) ;
BEGIN
  Dec_r0: dec2to4 PORT MAP ( w(1 DOWNTO 0), m(0), y(3 DOWNTO 0) );
  Dec_r1: dec2to4 PORT MAP ( w(1 DOWNTO 0), m(1), y(7 DOWNTO 4) );
  Dec_r2: dec2to4 PORT MAP ( w(1 DOWNTO 0), m(2), y(11 DOWNTO 8) );
  Dec_r3: dec2to4 PORT MAP ( w(1 DOWNTO 0), m(3), y(15 DOWNTO 12) );
  Dec_left: dec2to4 PORT MAP ( w(3 DOWNTO 2), En, m ) ;
END Structure ;

## Slide 24
VHDL code for Example 2 (2)
ARCHITECTURE Structure OF dec4to16 IS
  COMPONENT dec2to4
    PORT ( w : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
    En : IN STD_LOGIC ;
    y : OUT STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
  END COMPONENT ;
SIGNAL m : STD_LOGIC_VECTOR(3 DOWNTO 0) ;
BEGIN
  G1: FOR i IN 0 TO 3 GENERATE
  Dec_ri: dec2to4 PORT MAP ( ….………., ……….….., …………...);
  END GENERATE ;
  Dec_left: dec2to4 PORT MAP ( w(3 DOWNTO 2), En, m ) ;
END Structure ;

## Slide 25
VHDL code for Example 2 (2)
ARCHITECTURE Structure OF dec4to16 IS
  COMPONENT dec2to4
    PORT ( w : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
    En : IN STD_LOGIC ;
    y : OUT STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
  END COMPONENT ;
SIGNAL m : STD_LOGIC_VECTOR(3 DOWNTO 0) ;
BEGIN
  G1: FOR i IN 0 TO 3 GENERATE
  Dec_ri: dec2to4 PORT MAP (w(1 DOWNTO 0), m(i), y(4*i+3 DOWNTO 4*i));
  END GENERATE ;
  Dec_left: dec2to4 PORT MAP ( w(3 DOWNTO 2), En, m ) ;
END Structure ;

## Slide 26
Example 3: Up-or-down Free Running Counter

## Slide 27
Up-or-down Free Running Counter (1)
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity up_or_down_counter is
  generic(
  WIDTH: natural:=4;
  UP: natural:=0
  );
  port(
  clk, reset: in std_logic;
  q: out std_logic_vector(WIDTH-1 downto 0)
  );
end up_or_down_counter;

## Slide 28
Up-or-down Free Running Counter (2)
architecture mixed of up_or_down_counter is
  signal r_reg: unsigned(WIDTH-1 downto 0);
  signal r_next: unsigned(WIDTH-1 downto 0);
begin
-- register
  process(clk,reset)
  Begin
    if (reset='1') then
    r_reg <= (others=>'0');
    elsif (clk'event and clk='1') then
    r_reg <= r_next;
    end if;
end process;

## Slide 29
Up-or-down Free Running Counter (3)
-- next-state logic
inc_gen: -- incrementor
if UP=1 generate
r_next <= r_reg + 1;
end generate;
dec_gen: --decrementor
if UP/=1 generate
r_next <= r_reg – 1;
end generate;
-- output logic
q <= std_logic_vector(r_reg);
end mixed;

## Slide 30
Example 4: Up-and-down Free Running Counter

## Slide 31
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity up_and_down_counter is
generic(WIDTH: natural:=4);
  port(
    clk, reset: in std_logic;
    mode: in std_logic;
    q: out std_logic_vector(WIDTH-1 downto 0)
  );
end up_and_down_counter;
Up-and-down Free Running Counter (1)

## Slide 32
architecture mixed of up_or_down_counter is
  signal r_reg: unsigned(WIDTH-1 downto 0);
  signal r_next: unsigned(WIDTH-1 downto 0);
begin
-- register
  process(clk,reset)
  Begin
    if (reset='1') then
    r_reg <= (others=>'0');
    elsif (clk'event and clk='1') then
    r_reg <= r_next;
    end if;
end process;
Up-and-down Free Running Counter (2)

## Slide 33
-- next-state logic
  r_next <= r_reg + 1 when mode='1' else
  r_reg - 1;
-- output logic
  q <= std_logic_vector(r_reg);
end arch;
Up-and-down Free Running Counter (3)

## Slide 34
Example 5: Variable Rotator: Block Diagram

## Slide 35
a(15) a(14) a(13) a(12) a(11) a(10) a(9) a(8) a(7) a(6) a(5) a(4) a(3) a(2) a(1) a(0)
<<< 3
a(12) a(11) a(10) a(9) a(8) a(7) a(6) a(5) a(4) a(3) a(2) a(1) a(0) a(15) a(14) a(13)
y <= a(12 downto 0) & a(15 downto 13);
a(15) a(14) a(13) a(12) a(11) a(10) a(9) a(8) a(7) a(6) a(5) a(4) a(3) a(2) a(1) a(0)
<<< 5
a(10) a(9) a(8) a(7) a(6) a(5) a(4) a(3) a(2) a(1) a(0) a(15) a(14) a(13) a(12) a(11)
y <= a(10 downto 0) & a(15 downto 11);
Fixed rotation

## Slide 36
a(15) a(14) a(13) a(12) a(11) a(10) a(9) a(8) a(7) a(6) a(5) a(4) a(3) a(2) a(1) a(0)
<<< L
a(……) a(……...) . . . . . . . . . . . . . . a(1) a(0) a(15) a(14) . . . . . . . a(……….) a(……….)
y <= a(………………..) & a(…………………..);
Fixed rotation by L positions
a(15) a(14) a(13) a(12) a(11) a(10) a(9) a(8) a(7) a(6) a(5) a(4) a(3) a(2) a(1) a(0)
<<< L
a(15-L) a(15-L-1) . . . . . . . . . . . . . . a(1) a(0) a(15) a(14) . . . . . . . a(15-L+2) a(15-L+1)
y <= a(15-L downto 0) & a(15 downto 15-L+1);

## Slide 37
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY fixed_rotator_left_16 IS
  GENERIC ( L : INTEGER := 1);
  PORT ( a : IN STD_LOGIC_VECTOR(15 DOWNTO 0);
  y : OUT STD_LOGIC_VECTOR(15 DOWNTO 0) ) ;
END fixed_rotator_left_16 ;
ARCHITECTURE dataflow OF fixed_rotator_left_16 IS
BEGIN
y <= a(15-L downto 0) & a(15 downto 15-L+1);
END dataflow ;
VHDL code for a Fixed 16-bit Rotator

## Slide 38
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
ENTITY variable_rotator_16 is
  PORT(
  A : IN STD_LOGIC_VECTOR(15 downto 0);
  B : IN STD_LOGIC_VECTOR(3 downto 0);
  C : OUT STD_LOGIC_VECTOR(15 downto 0)
  );
END variable_rotator_16;
ARCHITECTURE structural OF variable_rotator_16 IS
  TYPE array16 IS ARRAY (0 to 4) OF
  STD_LOGIC_VECTOR(15 DOWNTO 0);
  SIGNAL Al : array16;
  SIGNAL Ar : array16;
Structural code for a Fixed 16-bit Rotator (1)

## Slide 39
BEGIN
Al(0) <= A;
  G: FOR i IN 0 TO 3 GENERATE
    ROT_I: ENTITY work.fixed_rotator_left_16(dataflow)
    GENERIC MAP (L => ………)
    PORT MAP ( a => ……….. ,
    y => ………..);
    MUX_I: ENTITY work.mux2to1_16(dataflow)
    PORT MAP (w0 => …………..,
    w1 => …………..,
    s => …………..,
    f => ……………);
  END GENERATE;
C <= Al(4);
END structural;
Structural code for a Fixed 16-bit Rotator (2)

## Slide 40
BEGIN
Al(0) <= A;
  G: FOR i IN 0 TO 3 GENERATE
    ROT_I: ENTITY work.fixed_rotator_left_16(dataflow)
    GENERIC MAP (L => 2** i)
    PORT MAP ( a => Al(i) ,
    y => Ar(i));
    MUX_I: ENTITY work.mux2to1_16(dataflow)
    PORT MAP (w0 => Al(i),
    w1 => Ar(i),
    s => B(i),
    f => Al(i+1));
  END GENERATE;
C <= Al(4);
END structural;
Dataflow VHDL code for a variable 16-bit rotator (3)

## Slide 41
BEGIN
  Al(0) <= A;
  G:
  FOR i IN 0 TO 3 GENERATE
    Ar(i) <= ……………………………….;
    Al(i+1) <= …………………………….;
  END GENERATE;
  C <= Al(4);
END dataflow;
Dataflow code for a Fixed 16-bit Rotator (2)

## Slide 42
BEGIN
  Al(0) <= A;
  G:
  FOR i IN 0 TO 3 GENERATE
    Ar(i) <= Al(i)(15-2**i downto 0) & Al(i)(15 downto 15-2**i+1);
    Al(i+1) <= Al(i) when B(i)=‘0’ else Ar(i);
  END GENERATE;
  C <= Al(4);
END dataflow;
Dataflow code for a Fixed 16-bit Rotator (2)

## Slide 43
Non-synthesizable VHDL

## Slide 44: Delays
Delays are not synthesizable
Statements, such as
wait for 5 ns
a <= b after 10 ns
will not produce the required delay, and
should not be used in the code intended
for synthesis.

## Slide 45: Initializations
Declarations of signals (and variables)
with initialized values, such as
SIGNAL a : STD_LOGIC := ‘0’;
cannot be synthesized, and thus should
be avoided.
If present, they will be ignored by the
synthesis tools.
Use set and reset signals instead.

## Slide 46: Dual-edge triggered register/counter (1)
In FPGAs register/counter can change only
at either rising (default) or falling edge of the
clock.
Dual-edge triggered clock is not synthesizable
correctly, using either of the descriptions
provided below.

## Slide 47: Dual-edge triggered register/counter (2)
PROCESS (clk)
BEGIN
IF (clk’EVENT AND clk=‘1’ ) THEN
counter <= counter + 1;
ELSIF (clk’EVENT AND clk=‘0’ ) THEN
counter <= counter + 1;
END IF;
END PROCESS;

## Slide 48: Dual-edge triggered register/counter (3)
PROCESS (clk)
BEGIN
IF (clk’EVENT) THEN
counter <= counter + 1;
END IF;
END PROCESS;
PROCESS (clk)
BEGIN
counter <= counter + 1;
END PROCESS;

## Slide 49: References
Stephen Brown and Zvonko Vranesic. 2004. Fundamentals of Digital Logic with VHDL Design. McGraw-Hill, Inc., New York, NY, USA.
https://ece.gmu.edu/coursewebpages/ECE/ECE545/F10/viewgraphs/ECE545_lecture_8_regular.pdf

## Slide 50: Questions?