## Slide 1
EEL4712 Digital Design

## Slide 2
Aliases

## Slide 3: Aliases
Syntax:
ALIAS name : type := expression;
Example:
signal IR : std_logic_vector(31 downto 0);
alias IR_opcode : std_logic_vector(5 downto 0) is IR(31 downto 26);
alias IR_reg1_addr : std_logic_vector(4 downto 0) is IR(25 downto 21);
alias IR_reg2_addr : std_logic_vector(4 downto 0) is IR(20 downto 16);

## Slide 4
Constants

## Slide 5: Constants
Syntax:
CONSTANT name : type := value;
Examples:
CONSTANT init_value : STD_LOGIC_VECTOR(3 downto 0) := "0100";
CONSTANT ANDA_EXT : STD_LOGIC_VECTOR(7 downto 0) := X"B4";
CONSTANT counter_width : INTEGER := 16;
CONSTANT buffer_address : INTEGER := 16#FFFE#;
CONSTANT clk_period : TIME := 20 ns;
CONSTANT strobe_period : TIME := 333.333 ms;

## Slide 6: Constants - Features
Constants can be declared in a
PACKAGE, ENTITY, ARCHITECTURE
When declared in a PACKAGE, the constant
is truly global, for the package can be used
in several entities.
When declared in an ARCHITECTURE, the
constant is local, i.e., it is visible only within this architecture.
When declared in an ENTITY declaration, the constant
can be used in all architectures associated with this entity.

## Slide 7
Packages

## Slide 8: Explicit Component Declaration versus Package
Explicit component declaration is when you declare components in main code
  When have only a few component declarations, this is fine
  When have many component declarations, use packages for readability
Packages also help with portability and sharing of libraries among many users in a company
Remember, the actual instantiations always take place in main code
  Only the declarations can be in main code or package

## Slide 9: METHOD #2: Package component declaration
Components declared in package
Actual instantiations and port maps always in main code

## Slide 10: Packages
Instead of declaring all components can declare all components in a PACKAGE, and INCLUDE the package once
  This makes the top-level entity code cleaner
  It also allows that complete package to be used by another designer
A package can contain
  Components
  Functions, Procedures
  Types, Constants

## Slide 11: Package – example (1)
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
PACKAGE GatesPkg IS
  COMPONENT mux2to1
  PORT (w0, w1, s : IN STD_LOGIC ;
  f : OUT STD_LOGIC ) ;
  END COMPONENT ;
  COMPONENT priority
  PORT (w : IN STD_LOGIC_VECTOR(3 DOWNTO 0) ;
  y : OUT STD_LOGIC_VECTOR(1 DOWNTO 0) ;
  z : OUT STD_LOGIC ) ;
  END COMPONENT ;

## Slide 12: Package – example (2)
  COMPONENT dec2to4
  PORT (w : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
  En : IN STD_LOGIC ;
  y : OUT STD_LOGIC_VECTOR(0 TO 3) ) ;
  END COMPONENT ;
  COMPONENT regn
  GENERIC ( N : INTEGER := 8 ) ;
  PORT ( D : IN STD_LOGIC_VECTOR(N-1 DOWNTO 0) ;
  Enable, Clock : IN STD_LOGIC ;
  Q : OUT STD_LOGIC_VECTOR(N-1 DOWNTO 0) ) ;
  END COMPONENT ;

## Slide 13: Package – example (3)
  constant ADDAB : std_logic_vector(3 downto 0) := "0000";
  constant ADDAM : std_logic_vector(3 downto 0) := "0001";
  constant SUBAB : std_logic_vector(3 downto 0) := "0010";
  constant SUBAM : std_logic_vector(3 downto 0) := "0011";
  constant NOTA : std_logic_vector(3 downto 0) := "0100";
  constant NOTB : std_logic_vector(3 downto 0) := "0101";
  constant NOTM : std_logic_vector(3 downto 0) := "0110";
  constant ANDAB : std_logic_vector(3 downto 0) := "0111";
END GatesPkg;

## Slide 14: Package usage (1)
LIBRARY ieee ;
USE ieee.std_logic_1164.all ;
USE work.GatesPkg.all;
ENTITY priority_resolver1 IS
PORT (r : IN STD_LOGIC_VECTOR(5 DOWNTO 0) ;
s : IN STD_LOGIC_VECTOR(1 DOWNTO 0) ;
clk : IN STD_LOGIC;
en : IN STD_LOGIC;
t : OUT STD_LOGIC_VECTOR(3 DOWNTO 0) ) ;
END priority_resolver1;
ARCHITECTURE structural OF priority_resolver1 IS
SIGNAL p : STD_LOGIC_VECTOR (3 DOWNTO 0) ;
SIGNAL q : STD_LOGIC_VECTOR (1 DOWNTO 0) ;
SIGNAL z : STD_LOGIC_VECTOR (3 DOWNTO 0) ;
SIGNAL ena : STD_LOGIC ;

## Slide 15: Package usage (2)
BEGIN
u1: mux2to1 PORT MAP ( w0 => r(0) ,w1 => r(1),s => s(0), f => p(0));
u2: mux2to1 PORT MAP ( w0 => r(4) ,w1 => r(5),s => s(1),f => p(3));
u3: priority PORT MAP (w => p, y => q, z => ena);
u4: dec2to4 PORT MAP ( w => q, En => ena, y => z);
u5: regn GENERIC MAP ( N => 4)
PORT MAP ( D => z , Enable => En ,Clock => Clk, Q => t );
p(1) <= r(2);
p(2) <= r(3);
END structural;

## Slide 16
Mixing Design Styles Inside
of an Architecture

## Slide 17: VHDL Design Styles

## Slide 18: Mixed Style Modeling
  architecture ARCHITECTURE_NAME of ENTITY_NAME is
  Here you can declare signals, constants, types, etc.
  Component declarations
  begin
  Concurrent statements:
    Concurrent simple signal assignment
    Conditional signal assignment
    Selected signal assignment
    Generate statement
    Component instantiation statement
    Process statement
      inside process you can use only sequential statements
  end ARCHITECTURE_NAME;
Concurrent Statements

## Slide 19: PRNG Example (1)
library IEEE;
use IEEE.STD_LOGIC_1164.all;
use work.prng_pkg.all;
ENTITY PRNG IS
PORT( Coeff : in std_logic_vector(4 downto 0);
Load_Coeff : in std_logic;
Seed : in std_logic_vector(4 downto 0);
Init_Run : in std_logic;
Clk : in std_logic;
Current_State : out std_logic_vector(4 downto 0));
END PRNG;
ARCHITECTURE mixed OF PRNG is
signal Ands : std_logic_vector(4 downto 0);
signal Sin : std_logic;
signal Coeff_Q : std_logic_vector(4 downto 0);
signal Shift5_Q : std_logic_vector(4 downto 0);

## Slide 20: PRNG Example (2)
-- Data Flow
G: FOR I IN 0 TO 4 GENERATE
Ands(I) <= Coeff_Q(I) AND Shift5_Q(I);
END GENERATE;
Sin <= Ands(0) XOR Ands(1) XOR Ands(2) XOR Ands(3) XOR Ands(4);
Current_State <= Shift5_Q;
-- Behavioral
Coeff_Reg: PROCESS(Clk)
BEGIN
IF Clk'EVENT and Clk = '1' THEN
IF Load_Coeff = '1' THEN
Coeff_Q <= Coeff;
END IF;
END IF;
END PROCESS;
-- Structural
Shift5_Reg : Shift5 PORT MAP ( D => Seed,
Load => Init_Run,
Sin => Sin,
Clock => Clk,
Q => Shift5_Q);
END mixed;

## Slide 21: References
https://ece.gmu.edu/coursewebpages/ECE/ECE545/F18/viewgraphs/ECE545_lecture_8_regular.pdf

## Slide 22: Questions?