## Slide 1
EEL4712 Digital Design
(Midterm 3 review)

## Slide 2: CDC
When the behavior of a circuit demonstrates some amount of randomness, it is likely that the output of a FF is:
  metastable
When synchronizing a single bit across clock domains, what type of synchronizer should you use?
  Dual flop
In what situation can a dual-flop synchronizer be used for multiple bits?
  When the input is guaranteed to change by only 1 bit at a time (e.g., gray coding).
Notes: With a dual flop, the output is either the previous value or the correct value. For multiple bits, the output could be incorrect.

## Slide 3: CDC
When synchronizing multiple bits across clock domains and don’t care about throughput, what type of synchronizer should you use?
  Handshake or mux recirculation
When synchronizing multiple bits across clock domains and throughput is important, what type of synchronizer should you use?
  FIFO
In what situation can dual-flop synchronizers be used to synchronize multiple bits?
  When only one bit changes

## Slide 4: CDC
When will metastability happen?
  Asynchronous signals
  Multiple clocks
At what points in the following circuit will metastability eventually occur?

## Slide 5: Combinational Loops
Describe what happens when the following VHDL code is simulated:
process(count)
begin
count <= count + 1;
end process;
  Infinite simulation loop, simulation will freeze and report that and iteration limit was reached

## Slide 6: BUS
1) FPGA synthesis replaces tristates with what type of component?
  Muxes
Draw a schematic of the FPGA mux-based circuit that would be synthesized for the following bus structure.

## Slide 7: Assert – Examples (3)
-- used in modeling flip-flops to check for timing problems
check: process
begin
wait until clk'event and clk='1';
assert D'stable(setup_time)
report "Setup Time Violation"
severity error;
wait for hold_time;
assert D'stable(hold_time)
report "Hold Time Violation"
severity error;
end process check;

## Slide 8: Assertion Example
Write an assertion for a bus access
  A, B, C, and D should not write at the same time on the bus

## Slide 9
What are the assertions and what is the purpose of using them?
What is the purpose of using SoCs?
  Reduced cost and better performance
Why is risky to use third-party IPs?
  Security and trust issues
    E.g., hardware Trojans

## Slide 10: Simon Cipher
Assume you are given a modified version of the Simon Cipher from Lab 6 that can support a variable number of rounds. How many cycles (ignoring initialization) will it take to encrypt the plaintext, “This is a password”, if your block size is 32 bits and the number of rounds is 20? Each round is one cycle and each ASCII character is 8 bits.
  “This is a password” is 18 ASCII char = 18*8 = 144 bits. 144 bits /32 bits per block = 5 blocks. 5 blocks*20 cycles = 100 cycles.

## Slide 11
How many bits are in each MIPS instruction?
  32
How many registers are in the MIPS register file?
  32
What is the purpose of the data stored into register 31 during a jump and link instruction?
  Function return address
What is the difference between a jump and branch instruction?
  A jump is unconditional and uses an absolute address instead of an offest

## Slide 12: MIPS Performance
What are the stages in a pipelined processor?
  Fetch
  Decode
  Execute
  Memory
  Writeback
Calculate the program Execution time for 1000 instructions a single cycle MIPS processor when the clock length is 10 ns.
  # instructions x CPI x TC = 1000 x 1 x 10 x 10^-9 = 10 μs

## Slide 13: MIPS Performance
Types of hazards in a pipelined processor?
  Data hazard: register value not written back to register file yet
  Control hazard: next instruction not decided yet (caused by branches)

## Slide 14: Questions?