## Slide 1: Introduction to HW Security & Trust
Fall 2023
University of Florida
Dr. Farimah Farahmandi

## Slide 2: Acknowledgement
Reference Book
  M. Tehranipoor and C. Wang, Introduction to Hardware Security and Trust, Springer, 2011
  Thanks to many colleagues, students, collaborators, etc. for their help and support over the past many years in putting the content of the book and the slides together.
Notes: 2

## Slide 3: EEE4714 / EEE5716
Title: “Introduction to Hardware Security and Trust”
Instructor
  Farimah Farahmandi, Yangbin Wang Rising Star Endowed Professor, ECE Department
Meeting time
  1:55 – 2:45pm Tuesday
  1:55 – 3:50pm Thursday
Meeting place
  NEB 202 (Online for EDGE)
Prerequisites
  EEE3701C: Digital Logic (or equivalent)
  Self-contained
  A brief overview of VLSI design and test will be given

## Slide 4: STAs for the Class
Md Sami Ul Islam
  PhD Student, Dept of ECE
  Email: md.sami@ufl.edu
  Office Hour: Thur 4-5pm
Md Rafid Muttaki
  PhD Student, Dept of ECE
  Email: m.muttaki@ufl.edu
  Office Hour: Tue 11 am-12 pm
Sajeed Mohammad
  PhD Student, Dept of ECE
  Email: mlnu@ufl.edu
  Office Hour: Wed 3-4pm
Office Hours for the Instructor:
Tuesdays 3-4pm, Online

## Slide 5: Overview of Course Content
Cryptographic hardware:
  Vulnerabilities, processing overhead
Attacks:
  Physical, invasive, non-invasive/side-channel
Physically unclonable functions (PUFs)
True random number generation (TRNG)
Anti-piracy:
  Watermarking, passive and active hardware metering
FPGA security
  Trusted design in FPGAs
Hardware Trojan detection and prevention
Counterfeit detection and avoidance

## Slide 6: Goals
Learning the state-of-the-art security primitives and methods as well as emerging technologies and security trends
Integration of security as a design metric, not as an afterthought for the system
Protection of the design intellectual property against piracy and tampering
Better understanding of attacks and providing countermeasures against them
Better understanding of vulnerabilities in design and fabrication processes
Better understanding of the electronic component supply chain vulnerabilities

## Slide 7: More to Read …
Reading
  Papers from the contemporary literature
Further possible reading
  Mihir Bellare and Phil Rogaway, Introduction to Modern Cryptography
  Ross J. Anderson. Security Engineering: A guide to building dependable distributed systems. John Wiley and Sons, 2001
  Matt Bishop, Computer Security: Art and Science, Addison-Wesley, 2003
  William Stallings. Cryptography and Network Security, Fourth edition, 2007
  M. Tehranipoor and F. Koushanfar, "A Survey of Hardware Trojan Taxonomy and Detection," IEEE Design and Test of Computers, 2010.
  M. Tehranipoor, H. Salmani, and X. Zhang, Integrated Circuit Authentication: Hardware Trojans and Counterfeit Detection, Springer July 2013.
  U. Guin, D. DiMase, and M. Tehranipoor, “Counterfeit Integrated Circuits: Detection, Avoidance, and the Challenges Ahead,” Journal of Electronic Testing: Theory and Applications (JETTA), Feb. 2014.

## Slide 8: More to Watch!
Videos
What's inside a microchip? http://www.youtube.com/watch?v=GdqbLmdKgw4
Zoom Into a Microchip http://www.youtube.com/watch?v=Fxv3JoS1uY8
Public Key Cryptography: RSA Encryption: http://www.youtube.com/watch?v=wXB-V_Keiu8
Counterfeit Electronics Could Be Dangerous, Funding Nefarious People http://www.youtube.com/watch?v=dbZiUe6guxc
How Computers and Electronics Are Recycled http://www.youtube.com/watch?v=Iw4g6H7alvo
Counterfeit Electronic Components Process http://www.youtube.com/watch?v=5vN_7NJ4qYA
Counterfeit Inspection http://www.youtube.com/watch?v=MbQUvu2LN6o
Gold from waste circuit electronics https://www.youtube.com/watch?v=4yGPm1U7U6s
Introduction to Hardware Hacking and Reverse Engineering https://www.youtube.com/watch?v=Q08jA2vVXfQ

## Slide 9: Grading and Project
Grading (Five components)
  One Midterm Exam: 20%
  One Final Exam: 20%
  Project Demo/Report: 20%
  Student Presentation: 15%
  2-3 HW Assignments (one before Midterm and another after Midtrerm): 15%
  2-3 Pop Quizzes, 10%
  This is subject to change
Project
  Groups of 3-4 for on-site students and individual for EDGE students
  Either propose or select from my list of potential projects/datasets
  Some projects involve hardware component (Xilinx FPGA development board)

## Slide 10: Software Tools Needed for Projects and HWs
PC or Mac or Linux Platforms are OK.
Statistical analysis of the attacks
  R statistical computing package (more info later)
Verilog/VHDL Tools:
  Synopsys / Xilinx design flow
Projects Involving FPGA Development Board
  Xilinx Vivado Synthesis tools (student edition would suffice)

## Slide 11: Course Outline
Introduction to Hardware Security & Trust
Introduction to Cryptography
Basics of VLSI Design and Test
Security Based on Physically Unclonability and Disorder
Hardware Metering
Watermarking of HW IPs
Physical Attacks and Tamper resistance
Side Channel Attacks and Countermeasures, Countermeasures for Embedded Microcontrollers
Fault Injection Attacks
Trusted Design in FPGAs
Security in Embedded Systems
Security for RFID Tags
Hardware Trojans: IC Trust (Taxonomy and Detection)
Hardware Trojans: IP Trust (Detection)
Design for Hardware Trust
Protecting against Scan-based Side Channel Attacks
Secure JTAG
Counterfeit Detection and Avoidance

## Slide 12: NSF SFS Opportunity (New)
The National Science Foundation (NSF) has awarded the University of Florida funding for 17 CyberScholars for the period 2017-2022.
Highly prestigious CyberCorps®: Scholarship For Service (SFS)
The SFS program is offered by the NSF and co-sponsored by the Department of Homeland Security (DHS).
Scholarship recipients shall pursue academic programs in: Cybersecurity with emphasis on hardware and systems security (HSS)
Domestic students are eligible to apply
The program will fund the final:
  Two years of a master's-level program
  Two-Three years of study for the bachelor's degree
  Three years of research-based doctoral-level study

## Slide 13: NSF SFS Opportunity (New)
Program Benefits
  Stipend: $22,500 per year for undergraduate students; $34,000 per year for master's degree students and $34,000 per year for doctoral students.
  Full tuition and education related fees.
  Health insurance reimbursement (up to $3000 per year).
  Professional development allowance (travel, professional certification etc. (up to $4000 per year) and a book allowance (up to $2,000 per year).
  Government summer internships and job opportunities with the world’s leading security organization.
Focused on Cybersecurity Education, the Scholarship For Service program gives students scholarship funds in exchange for service in the federal government for a period equivalent to the length of their scholarship (up to three years).
Visit https://www.sfs.opm.gov/ for more information

## Slide 14: Hardware Security
Cybersecurity experts have traditionally assumed that the hardware underlying information systems is secure and trusted.
However, such assumption is no longer true.

## Slide 15: What is Hardware?
SOC
Electronic System
System Hardware – acts as the “root-of-trust”: PCB → IC (SoC | µP)
µP

## Slide 16: Example Attack
Roy Zoppoth stands over a Xerox 914 copy machine, the world's first, which was used in soviet embassies all over the world. The machine was so complex that the CIA used a tiny camera designed by Zoppoth to capture documents copied on the machine by the soviets and retrieved them using a "Xerox repairman" right under the eyes of soviet security.
Photo from edit international courtesy of Roy Zoppoth

## Slide 17: Motivation – HW Security
HW security is becoming increasingly important
  Hardware security sneaks into PCs, Robert Lemos, CNET News.com, 3/16/05
  Microsoft reveals hardware security plans, concerns remain, Robert Lemos, SecurityFocus 04/26/05
  Princeton Professor Finds No Hardware Security In E-Voting Machine, Antone Gonsalves, InformationWeek 02/16/07
  Secure Chips for Gadgets Set to Soar, John P. Mello Jr. TechNewsWorld, 05/16/07
  Army requires security hardware for all PCs, Cheryl Gerber, FCW.com, 7/31/2006
  Visit Facebook group on Hardware Security

## Slide 18: Example Attack
Pentagon’s ‘Kill Switch': Urban Myth?
The Pentagon is worried that "backdoors" in computer processors might leave the American military vulnerable to an instant electronic shut-down. Those fears only grew, after an Israeli strike on an alleged nuclear facility in Syria. Many speculated that Syrian air defenses had been sabotaged by chips with a built-in ‘kill switch" — commercial off-the-shelf microprocessors in the Syrian radar might have been purposely fabricated with a hidden “backdoor” inside. By sending a preprogrammed code to those chips, an unknown antagonist had disrupted the chips’ function and temporarily blocked the radar."
This all had a very familiar ring to it. Those with long memories may also recall exactly the same scenario before: air defenses knocked out by the secret activation of code smuggled though in commercial hardware.
This was back in 1991 and the first Iraq War, when the knockout blow was administered by a virus carried by a printer : One printer, one virus, one disabled Iraqi air defense.

## Slide 19: Example Attack
DHS: Imported Consumer Tech Contains Hidden Hacker Attack Tools
  Top homeland securities have admitted instances where along with software, hardware components that are being imported from foreign parties and used in different US systems are being compromised and altered to enable easier cyber-attacks.
The Hunt for Kill Switch, IEEE Spectrum 2008
  Increasing threat to hardware due to globalization
  Extremely difficult to detect kill switches (utilized by enemies to damage/destroy opponent artillery during critical missions) as well as intentional backdoors (to enable remote control of chips without user knowledge), which may have huge consequences
  Example: Syrian’s Radar during Israeli attack, French Government using kill switches intentionally as a form of active defense to damage the chips if they fall in hostile hands, and more...

## Slide 20: Example Attack
Fake Cisco routers risk "IT subversion”
  An internal Federal Bureau of Investigation presentation states that counterfeit Cisco routers imported from China may cause unexpected failures in American networks. The equipment could also leave secure systems open to attack through hidden backdoors.
  $76 million fake Cisco routers
Energy Theft Going From Bad to Worse
  Tampering with “smart” meters
    Oil, electricity, gas, …
  $1B loss in CT because of electricity theft

## Slide 21: Example Attack
The deadly world of fake medicine – CNN.com
  A counterfeit medication or a counterfeit drug is a medication or pharmaceutical product which is produced and sold with the intent to deceptively represent its origin, authenticity or effectiveness.
Medical Device Security
  Incorporating security is sometimes considered expensive
  Implantable devices: e.g., Heart rate monitor
    Incorporating Security could potentially reduce the life-time of the device by 30%
    Attacking these device could result in loss of lives

## Slide 22: Example Attack
Physical Attacks on Chip IDs
  Extracting secret keys
Side-Channel Attacks
  Power Analysis, Timing Analysis, EM Analysis
Tampering with Electronic Devices
  Captured Drone by Iran
Counterfeit Integrated Circuits
  Multi-billion dollar business

## Slide 23: Time for Smart Cards
By the end of 2006, Westerns European countries fully migrated to smart cards
  Voting: In Sweden you can vote with your smart card, which serves as a non-repudiation device
  Telecommunications: Many cellular phones come with smart cards in Europe and will soon be shipping in the United States.
  Mass Transit: British Air relies on rail and air connections more than most airports.
In 2006, ~27M contactless cards were in circulation in US, the number is estimated to top 100M by 2011
  E.g., homeland security has required the port workers to have smart ID cards (Jan, 2007)
  Entertainment: Most DSS (Digital Satellite Service) dishes in the U.S. have smart cards.

## Slide 24: Smart Cards Attack Architecture
The victim card is reached by the attacker through his NFC-equipped mobile phone connected to a NFC-equipped mobile phone in proximity of the card.
The phone close to the victim card can be instructed to run local attacks,
e.g., to extract and return the card access code, and the entire architecture can serve for relay attacks.
Source: Internet

## Slide 25: Smart Cards -- Attacks
Access Control: Smart Cards Under Attack - Literally, Ken Warren, Security Magazine, 03/17/2006
Keep Your Enemies Close: Distance Bounding Against Smartcard Relay Attacks, Saar Drimer and Steven J. Murdoch, USENIX SECURITY, 2007
Vulnerability Is Discovered In Security for Smart Cards, John Markoff, NY TIMES, 05/13/2002

## Slide 26: Smart Cards Attacks - Examples
Relay attack against a contactless smart card
Remote contactless cards attack

## Slide 27: Hardware level security attacks on smart cards
Source: Internet

## Slide 28: RFIDs
Radio-frequency identification (RFID) is the use of an object (typically referred to as an RFID tag) applied to or incorporated into a product, animal, or person for the purpose of identification and tracking using radio waves.
Most RFID tags contain at least two parts:
  An integrated circuit for storing and processing information, modulating and demodulating a radio-frequency (RF) signal, and other specialized functions.
  An antenna for receiving and transmitting the signal.
  Some are active (battery) and some others are passive

## Slide 29: RFIDs
29
Many applications in securing transactions,
  Inventory Control Container / Pallet Tracking
  ID Badges and Access Control
  Fleet Maintenance Equipment/Personnel Tracking in Hospitals
  Parking Lot Access and Control
  Car Tracking in Rental Lots
  Product Tracking through Manufacturing and Assembly
Challenge: Can we create security mechanisms light enough to be suitable for the RFIDs?
Notes: 29

## Slide 30: Piracy – Some True Stories…
In 2000, Chen Jin, finished Ph.D. in computer engineering at UT Austin
He went back to China, first to Motorola research and then to Jiaotong University as a faculty
In 2003, he supervised a team that created one of China's first homegrown DSP IC
Chen was named one of China’s brightest young scientists, funded his own lab, got a huge grant from the government
In 2006, it was revealed that he faked the chip, stealing the design from Texas Instruments!
Links to the article: 1, 2

## Slide 31: The Athens Affair
In March 8, 2005, Costas Tsalikidis, a 38-year-old Engineer working for Vodafone Greece committed suicide – linked to the scandal!
The next day, the prime minister got notified that his cell phone – and those of many other high-rank officials – were hacked!
Earlier in Jan, investigators had found rogue software installed on the Vodafone Greece by parties unknown
The scheme did not depend on the wireless nature
A breach in keeping keys in a file – Vodafone was fined €76 million December 2006!

## Slide 32: Interesting Articles
The Hunt for the Kill Switch, IEEE Spectrum, May 2008
J. Villasenor and M. Tehranipoor, “The Hidden Dangers of Chop Shop Electronics” IEEE Spectrum, Sep. 2013.
M. Tehranipoor, U. Guin, and S. Bhunia, "Invasion of the Hardware Snatchers: Fake Hardware Could Open the Door to Malicious Malware and Critical Failure," IEEE Spectrum, 2017.
S. Quadir, J. Chen, D. Forte, N. Asadi, S. Shahbaz, L. Wang, J. Chandy, and M. Tehranipoor, "A Survey on Chip to System Reverse Engineering," ACM Journal on Emerging Technologies in Computing Systems (JETC), 2015.
M. Alam, M. Tehranipoor, and U. Guin, "TSensors Vision, Infrastructure, and Security Challenges in Trillion Sensor Era," Journal of Hardware and Systems Security (HaSS), 2017.
K. Yang, H. Shen, D. Forte, S. Bhunia, and M. Tehranipoor, "Hardware-Enabled Pharmaceutical Supply Chain Security," ACM Transactions on Design Automation of Electronic Systems (TODAES), 2017.
F. Rahman, B. Shakya, X. Xu, D. Forte, and M. Tehranipoor, "Security Beyond CMOS: Fundamentals, Applications, and Roadmap," IEEE Transactions on VLSI (TVLSI), 2017.

## Slide 33: Evolution of Hardware Security and Trust
Prior to 1996: Coating, encapsulation, labeling, taping, … still many companies don’t spend much for securing their hardware
1996: Extracting secret keys using power analysis – started the side-channel signal analysis era
1998: Hardware unique ID
2002: Physically Unclonable Functions (PUFs), True Random Number Generation (TRNG), Hardware tagging
2004-2007: DARPA TRUST, Hardware trust
2008: DARPA IRIS Program – Reverse engineering, tampering, and reliability
2008: Counterfeit ICs
2012: Senate Armed Services – National Defense Authorization Act (NDAA) 2012
2014: DARPA SHIELD – Supply chain security
2015: DARPA LADS
More…

## Slide 34: Shift in the Industry’s Business Model
Vertical - one company
Synthesis
Fabrication
HDL
Place
Route
Horizontal (Dominant) – Two or more companies
Fabrication
Economy of scale:
The same fabrication facility serves many fabless companies
HDL
Synthesis
Placement
Routing

## Slide 35: Microelectronic Industry Business Model
Notes: Two points:
protection of design house against foundry
Ic providers against unauthorized

## Slide 36: The Global Microelectronics Market Size
The global microelectronics market size was valued at USD 318.15 billion in 2021 and it is expected to surpass around USD 455.67 billion by 2030 with a registered CAGR of 4.1% from 2022 to 2030.
Source: Internet

## Slide 37: Global Semiconductor Market 2020-2024
Source: Business Wire
Industry Trends, Share, Size, Growth, Opportunity and Forecast

## Slide 38: Leading-Edge Technology
The cost of building a full-scale, 300 mm wafer 65nm process chip fabrication plant is about $3bn

## Slide 39: What’s Next – Technology

## Slide 40: HW Threats
IP Vendor
System Integrator
Manufacturer
Any of these steps can be untrusted

## Slide 41: HW Threats
IP Vendor
System Integrator
Manufacture
Untrusted
IP Trust
IC Trust

## Slide 42: HW Threats
IP Vendor
System Integrator
Manufacture
Untrusted
IP Piracy
System Trust
IC Trust

## Slide 43: HW Threats
IP Vendor
System Integrator
Manufacture
Untrusted
IC Trust
IC Piracy (Counterfeiting)
Secure Manufacturing Test
Untrusted Foundry

## Slide 44: Design Process – Old Way
RTL->GL
Synthesis
RTL
GL
Layout +
STA
GDSII
ASIC Manufacturer
Design Specification
Cell & I/O
Libraries
Cell & I/O
GDSII

## Slide 45: Issues with Third-Party IP Design
System-on-Chip (SoC)
Notes: Another example: USB-based hardware trojans
FPGA devices

## Slide 46: Issues with Third-Party IP Design
Company X
Company Y
Company Z
Company W
Company V
System-on-Chip (SoC)
Notes: Another example: USB-based hardware trojans
FPGA devices

## Slide 47: Issues with Third-Party IP Design
Company X
Company Y
Company Z
Company W
Company V
System-on-Chip (SoC)
These companies are located across the world There is no control on the design process
Notes: Another example: USB-based hardware trojans
FPGA devices

## Slide 48: Design Process – New Way
RTL -> GL
Synth + DFT
RTL
GL
Layout
+ STA
GDSII
ASIC Manufacturer
Design Specification
Cell & I/O
Libraries
Cell & I/O
GDSII
RTL
RTL
RTL
GDSII
Soft IP
GL
Untrusted IPs
Hard IP
Firm IP
Soft IP
SOC Design Process

## Slide 49: Who Develops the IPs? Who Designs the ICs? Who Fabricates Them?

## Slide 50: Who Develops the IPs? Who Designs the ICs? Who Fabricates Them?
Every Where!
IP
IP
IP
DFT
GDSII
Fab
Assembly & Test
Ship to the market

## Slide 51: Untrusted System Integrator
ASIC Manufacturer
Design Specification
Hard IP
Soft IP
RTL -> GL
Synth + DFT
RTL
GL
Layout
+ STA
GDSII
Cell & I/O
Libraries
Cell & I/O
GDSII
RTL
RTL
RTL
GL
GDSII

## Slide 52: Counterfeiting
IP Owner
Foundry
Assembly
GDSII
0100100101110010000100100111000101010100101010000010100111111000000010001000011
Market
Google image

## Slide 53: Counterfeiting
IP Owner
Foundry
Assembly
GDSII
01001001011100100001001001110001010101001010100000101001111110000
Over-produced
ICs
Defective or
Out-of-spec
ICs
Market
Google image
Notes: Low yield wafers
Focus is on untrusted foundry and assembly

## Slide 54: IC Counterfeiting
Most prevalent attack today
Unauthorized production of wafers
It is estimated that counterfeiting is costing semiconductor industry more than several billion dollars per year
Over production
Defective parts
Off-spec parts
Cloned ICs
Recycled ICs

## Slide 55: IC Recycling Process
ICs taken off of PCBs
Refine recycled ICs
Resold as new
Critical Application
PCBs taken off of electronic systems
A recycling center
Identical:
Appearance, Function, Specification
Source: Images are taken from google
Consumer trends suggest that more gadgets are used in much shorter time – more e-waste
Notes: Foundry:
  A foundry can add functionality to the design
Detecting Trojans in ICs is very important for IC designers

## Slide 56: Supply Chain Vulnerabilities
IP Piracy

## Slide 57: Some Basic Definitions
Intellectual property represents the property of your mind or intellect - proprietary knowledge
The four legally defined forms of IP
  Patents When you register your invention with the government, you gain the legal right to exclude anyone else from manufacturing or marketing it
  Trademarks A trademark is a name, phrase, sound or symbol used in association with services or products
  Copyrights Copyright laws protect written or artistic expressions fixed in a tangible medium
  Trade secrets A formula, pattern, device or compilation of data that grants the user an advantage over competitors

## Slide 58: Some Basic Definitions (Cont’d)
Cryptography:
  crypto (secret) + graph (writing)
    the science of locks and keys
  The keys and locks are mathematical
  Underlying every security mechanism, there is a “secret”…
  We are going to talk some about the traditional crypto, but we will also show new forms of security based on other forms of HW-based secret

## Slide 59: What Does Secure Mean?
It has to do with an asset that has some value – think of what can be an asset!
There is no static definition for “secure”
Depends on what is that you are protecting your asset from
Protection may be sophisticated and unsophisticated
Typically, breach of one security makes the protection agent aware of its shortcoming
Notes: 59
Willie Sutton was asked why he robs banks, he says because “that’s where the money is”. So one can ask why attacking crypto systems, the answer is because that’s where the secret it.

## Slide 60: Typical Cycle in Securing a System
Predict potential breaches and vulnerabilities
Consider possible countermeasures, or controls
Either actively pursue identifying a new breach, or wait for a breach to happen
Identify the breach and work out a protected system again
Notes: 60

## Slide 61: Computer Security
No matter how sophisticated the protection system is – simple breaches could break-in
A computing system is a collection of hardware (HW), software (SW), storage media, data, and human interacting with them
Security of SW, data, and communication
HW security, is important and challenging
  Manufactured ICs are obscure
  HW is the platform running SW, storage and data
  Tampering can be conducted at many levels
  Easy to modify because of its physical nature
Notes: 61

## Slide 62: Definitions
Vulnerability: Weakness in the secure system
Threat: Set of circumstances that has the potential to cause loss or harm
Attack: The act of a human exploiting the vulnerability in the system
Computer security aspects
  Confidentiality: the related assets are only accessed by authorized parties
  Integrity: the asset is only modified by authorized parties
  Availability: the asset is accessible to authorized parties at appropriate times
Notes: 62

## Slide 63: Hardware Vulnerabilities
Physical Attacks
Trojan Horses
IP Piracy
IC Piracy & Counterfeiting
Backdoors
Tampering
Reverse Engineering
Notes: 63

## Slide 64: Adversaries
Individual, group or governments
  Pirating the IPs – illegal use of IPs
  Inserting backdoors, or malicious circuitries
  Implementing Trojan horses
  Reverse engineering of ICs
  Spying by exploiting IC vulnerabilities
System integrators
  Pirating the IPs
Fabrication facilities
  Pirating the IPs
  Pirating the ICs
Counterfeiting parties
  Recycling, cloned, etc.
Notes: 64

## Slide 65: Hardware Controls for Secure Systems
Hardware implementations of encryption
  Encryption has to do with scrambling to hide
Design locks or physical locks limiting the access
Devices to verify the user identities
Hiding signatures in the design files
Intrusion detection
Hardware boards limiting memory access
Tamper resistant
Policies and procedures
More …
Notes: 65

## Slide 66: Embedded Systems Security/IoTs
Security processing adds overhead
  Performance and power
Security is challenging in embedded systems/IoTs
  Size and power constraints, and operation in harsh environments
Security processing may easily overwhelm the other aspects of the system
Security has become a new design challenge that must be considered at the design time, along with other metrics, i.e., cost, power, area
Notes: 66

## Slide 67: Security Requirements in the IoT Era
Notes: 67

## Slide 68: Secure Embedded Systems - Design Challenges
Processing gap
Battery gap
Flexibility
  Multiple security objectives
  Interoperability in different environments
  Security processing in different layers
Tamper resistance
Assurance gap
Cost
Notes: 68

## Slide 69: Secret
Underlying most security mechanisms or protocols is the notion of a “secret”
  Lock and keys
  Passwords
  Hidden signs and procedures
  Physically hidden
Notes: 69

## Slide 70: Cryptography – History
Has been around for 2000+ years
In 513 B.C, Histiaeus of Miletus, shaved the slave’s head, tattooed the message on it, let the hair grow
Notes: 70

## Slide 71: Cryptography – Pencil & Paper Era
Caesar’s cipher: shifting each letter of the alphabet by a fixed amount!
  Easy to break
Cryptoquote: simple substitution cipher, permutations of 26 letters
  Using the dictionary and the frequencies, this is also easy to break
Plaintext: THE QUICK BROWN FOX JUMPS OVER THE LAZY DOG
Ciphertext: QEB NRFZH YOLTK CLU GRJMP LSBO QEB IXWV ALD
Notes: 71

## Slide 72: Cryptography – Mechanical Era
Around 1900, people realized cryptography has math and stat roots
German’s started a project to create a mechanical device to encrypt messages
Enigma machine  supposedly unbreakable
A few polish mathematicians got a working copy
The machine later sold to Britain, who hired 10,000 people to break the code!
They did crack it! The German messages were transparent to enemies towards the end of war
  Estimated that it cut the war length by about a year
British kept it secret until the last working Enigma!
Notes: 72

## Slide 73: Cryptography – Mechanical Era
Another German-invented code was Tunny (Lorenz cipher system)
Using a pseudorandom number generator, a seed produced a key stream ks
The key stream xor’d with plain text p to produce cipher c: c=pks
How was this code cracked by British cryptographers at Bletchley Park in Jan 1942?
A lucky coincidence!
German rotor stream cipher machines used by the German Army during World War II
Notes: 73

## Slide 74: Cryptography – Modern Era
First major theoretical development in crypto after WWII was Shannon’s Information Theory
Shannon introduced the one-time pad and presented theoretical analysis of the code
The modern era really started around 1970s
The development was mainly driven by banks and military system requirements
NIST developed a set of standards for the banks,
  DES: Data Encryption Standard
Notes: 74

## Slide 75: References
http://www.ecs.umass.edu/ece/labs/vlsicad/ece667/ece667.html

## Slide 76: Thank You!
Questions?